## Slide 1: Optical Box for Optical Computing
Optical Box operated under control of embedded computer for Optical Computing like Fourier Transform by a Lens or 2D Fourier Transform. Calculation price (or energy power per single math operation) of Optical Box is 5-10% or less of Discrete Processor calculation price. Optical Computing is not a universal panacea of Computing Industry. It has many limitations, need special knowledge, and need additional research in math, optics and algorithms.

## Slide 2: History
Optical Computing is not a modern idea or technology. Optical Computing idea was popular during 1980-1990. There are many publications and research exists, but until now, no one device sold for public.
Major technics used for Optical Computing is Fourier Transform by a Lens or 2D Fourier Transform.
During previous century electronic components was expensive, other components was unique and do not provide required quality to make product for everyone. Therefore, computing technology has been concentrated to manufactory Discrete Processors based on logic of switchers and transistors.

## Slide 3: What is Optical Computing
Numbers
  Real as Amplitude of Complex EMW Vector
Operations
    Rough calculations of Amplitude of Random Vector to Predefined Matrix multiplication
  Do all math calculations parallel with one step for all signal points
Operates with Complex EMW vectors
Rough Arithmetic Calculations
Using Interference and Diffraction of light (EMW)

## Slide 4: Light for Optical Computing

## Slide 5: Visible Light for Optical Computing

## Slide 6: Interference and Diffraction for Optical Computing

## Slide 7: Is Experiments with Light Interference and Diffraction Need a Deep Leaning?
An answer – No.
There are sold many DIY Kids to do experiments with Light Interference and Diffraction
  Laser Diode Pen Stick and printed lines and holes
  Fresnel Zone Plate used as a lens

## Slide 8: Ideal Light for Optical Computing
Monochrome
Polarized
Single Source

## Slide 9: Using Real Light for Optical Computing
Using Light Sources with short spectrum range emitted and small emitted area
  Lasers
  Laser Diodes
  Light Emitted Diodes
Using Light Detectors with short spectrum range accepted
  Different Sensor Types
Using Light Filters to short spectrum range
Polarize Light by Filters
  Some kind of Films
  Some kind of Surface Reflections
Combination all methods above
a
b
c

## Slide 10: Consumer chip market analysis results
My own research and analysis of price and characteristics of electronic components presented on consumer chip market (beginning of 2015), show that Optical Box for Optical Computing operated under control of embedded computer can be manufactured with follow properties:
Dimension of single Optical Box for Optical Computing do not exceed the dimension of modern Discrete Processor with cooling radiators.
Computing effectivity of Optical Box for Optical Computing (for special calculations) are compatible to computing effectivity of modern Discrete Processor of same size (with cooling radiators).
Manufacturing price of Optical Box for Optical Computing is chipper than manufacturing price of modern Discrete Processor and do not required so expensive equipment and buildings.
Calculation price (or energy power per single math operation) of Optical Box is 5-10% or less of Discrete Processor calculation price.
  Therefore, Optical Box do not required additional cooling system like modern Discrete Processor.

## Slide 11: Comparisons matrix of stock prices and energy power required
Processor Type | Xeon E5 |  | 
Chips for Full HD 1920 * 1080 50Hz |  | 1 | 8
Productivity | ~200GFlops | ~1GFlops | ~512GFlops
Stock price | ~1000USD | ~150USD | ~3000USD
Energy power | ~135W | ~0.1W | ~1W
Stock price/ Productivity | ~5USD/ GFlops | ~150USD/ GFlops | ~6USD/ GFlops
Energy power / Productivity | ~0.75W/ GFlops | ~0.1W/ GFlops | ~0.2W/ GFlops

## Slide 12: Trends Analysis
Analysis of trends show me that single Optical Box for Optical Computing with a size like the size of modern Discrete Processor with cooling radiators will have the bigger computing effectivity and smaller calculation price (or energy power per single math operation) then the same size Discrete Processor with cooling radiators.

## Slide 13: Why Optical Computing?
Optical Computing is not a universal panacea of Computing Industry. It has many limitations, need special knowledge, and need additional research in math, optics and algorithms.
With using Optical Computing a lot of money and energy spend to simple math calculation will be saved.

## Slide 14: Economics
Average computer mainframe electric bill can be 100K$/month and up.
Number of mainframes worldwide are hundreds.
Big part of money are spend to energy power for typical calculations that can be done with Optical Computing with price 90-95% or more less as usually.
Take part of money saved is a main aim for this project.
For example,
  Let 100 mainframes have average electric bill can be 100K$/month
  Let using Optical Computing will cut electric bill to 50%.
  If 10% of saved money will be spend to Optical Computing maintenance
  Then 100*100K$/month*50%*10% = 500K$/month can be spend as subscription plan for Optical Computing maintenance.
Hardware sales, third-party software licensing and consulting will generate additional money income for project.

## Slide 15: Planned Cash Income Sources
Subscription Plans
Hardware Sales
Third-Party Software Licensing
Consulting

## Slide 16: Applied Fields of Optical Computing
Video and Audio Processing.
Patterns Recognitions.
Trends Analysis.
Network Data Transmission.
Cryptography.
Scientific Calculations.
And more, more and more

## Slide 17: Who will use Optical Computing?
Banks and Brokerages to predict stock trends.
Medical Laboratory to analyze microscope images.
3D and 2D Designers to render images of scene.
Sound Recorders to remove noise or detect voice.
Robot Designers for computer vision or AI.
And more, more and more

## Slide 18: Hard & Soft
I intend to manufactory Optical Box for Optical Computing as 19’’ rack-mount case with an embedded control system and network interfaces. This manufacturing schema allow using Optical Box for Optical Computing as a Personal Device or as a Mainframe Part.
The Optical Box for Optical Computing will operate with other application and tools using web-based API (Application Program Interface) like REST, SOAP or similar. Plugins and Add-ons will be developed for the most popular applications like Adobe Photoshop, Solidworks, 3D Max, Ninjatrader, etc.

## Slide 19: Roadmap
A roadmap for project required 1 year to start and include
  R&D,
  Market Analysis,
  Negotiations,
  Agreements,
  Patents and Legal.

## Slide 20: R&D main steps
R&D include Optical Box design and Optical Box Emulator development.
Optical Box Emulator will allow test and demonstrate functionality to customers and investors without full Optical Box manufacturing process.
Optical Box design required Component Supplier Analysis to be first.

## Slide 21: Fourier transforming property of lenses

## Slide 22: Fourier Transform Usage Samples
To show how Optical Computing with 2D Fourier Transform can be used I develop some examples of image processing tools with 2D Discrete Fast Fourier Transform which is closed analogy of 2D Infinity Fourier Transform by Lens
  Image Resize,
  Image Blur,
  Piece of Image Position Detection.
Software Packages and Tools was used for samples development
  Microsoft Visual Studio 2013 C#
  EmguCV/OpenCV – C++ computer vision library (bitmap data management part)
  FFTWSharp/FFTW – C++ Discrete Fast Fourier Transform implementation

## Slide 23: Image Resize Fourier Transform Usage Sample

## Slide 24: Image Blur Fourier Transform Usage Sample

## Slide 25: Piece of Image Position Detection Fourier Transform Usage Sample

## Slide 26: Fresnel Diffraction

## Slide 27: Fresnel Zone Plate Binary & Sinusoidal

## Slide 28: Using Zone Plate for Optical Computing

## Slide 29: Optical Box Draft Model

## Slide 30: Optical Box Draft Design

## Slide 31: Optical Box Design Description
Chips of LD, DLPs and MIS are mount on one side of a Circuit Board in row with equal step. LD and MIP are placed at left and right DLPs are placed in the middle.
The Circuit Board is places at one side of a Frame
At another side of the Frame placed a Film with printed FZPs, a Polarizing Filter, a Color Filter and a Mirror
Sizes of the Circuit Board, the Film with FZPs, the Polarizing Filter, the Color Filter and the Mirror are equal
A number of printed FZPs is equal a number of DLPs plus two half-sized FZPs for LD and MIS
To remove wrong light rays LD, DLPs, FZPs and MIS have collimator shutters
Light from LD multiply time pass thru FZP and reflect from Mirror on a second side of the Frame or reflect from DLP on a first side of the Frame until MIS catch a ray.
Distances between a pair of LD-FZP or FZP-DLP or FZP-MIS are equal
DLP or MIS can be combined from number of chips
Some DLP can be replaced by mirrors to reduce number of DLP chips

## Slide 32: Optical Box Draft Design Description
A number of single Optical Boxes can by stacked or combined
DIPs and MISs can be placed as 1D or 2D arrays
Optical Box can be equipped by
  An internal memory to fast read MIS values and write DIPs values
  An embedded computer with embedded software
  An Ethernet port
  A front panel
  A power supply
  19’’ rack mount kids

## Slide 33: DLP Usage Notes
Usual DLP chip micro-mirrors have 3-state (3 micro-mirror reflection angle)
  Parked
  On or Off
  Technology to generate grayed image by fast switch between On and Off states used by video projectors is not applicable by Optical Computing.
  Solution Ways in case using DLP chip of micro-mirrors with limited states is
    Do calculations with 1-bit numbers and apply iteration math algorithms to up precision
    Use group of micro-mirrors to generate gray color
  Another way to use micro-mirrors with 3-state in binary mode in case of slow MIS is
    Transparent = Parked state
    Opaque = fast random switch between On and Off states.
      fast random switch between two states will generate average energy picture caused random diffraction pictures cached by MIS

## Slide 34: Optical Box Math
Optical Box Design do parallel math calculations of signals on DLP
Optical Box Design do not calculate Fourier transforming
Optical Box Design do calculate Some (Unknown, depended from device implementation) Matrix Multiplication transforming of signals on each FZP
Because Optical Box Design has more then two DLP
  Reverse of Unknown Matrix
    Can be calculated by experiments (during Optical Box Calibration)
    Can be saved for future use in embedded memory of Optical Box
    Can be used for calculation needed
  One DLP (if light is high polarized) or two DLP (if light is low polarized) can be used to correct total matrix production for calculation needed like Fourier transforming, Walsh-Hadamar transforming and etc.

## Slide 35: Optical Box Calibration Definition
  If Y = OUTPUT(X1,X2,X3,…) is an output from Optical Box with X1, X2, X3 … values of DLPs
  If F(X1,…,Xn-1) = max || OUTPUT(X1,…,Xn-1,X) - | X*M | || for all X
  If F(C1,…,Cn-1 ) = min F(X1,…,Xn-1) for all X1,…,Xn-1
  Then values C1,…,Cn-1 will be named Calibration for transformation matrix M and
  Y=| X*M | = OUTPUT(C1,…,Cn-1,X)
  Calculations can be done with PC and Optical Box together or within Optical Box only using embedded discrete computer

## Slide 36: Minimal Optical Box Calibration Size
Calibration allow to remove non-linear distortion due non-ideal conditions of single lens transformation.
    The main distortion for Interference and Diffraction of light caused by Non-Polarized light. Some materials can change light polarization during light reflection or pass thru transparent material.
      EMW consists of Electric and Magnetic Parts
        If light is Non-Polarized Electric(or Magnetic) Parts of two beams are not summarize as values but summarize as direct vectors so light detector catch average power for all cells and do not recognize Interference/Diffraction picture of two beams of light.
      Electric and Magnetic Parts of any EMW can be present as complex number or as a pair of real numbers
    Calibration which can remove distortion caused by Non-Polarized light must contains a pair of real calibration values for any output amplitude value at point as real number.

## Slide 37: Optical Box Calculations Precision
Fact
  Calculation with using optics calculations gives rough results
Solution Ways
  Same algorithms like sorting, brute force, branch-and-bounds and etc. do not need precision for all results but selected only. Selected results can by calculated traditional way or improved by additional math iteration algorithms of selected results.
  There are many step-by-step math iteration algorithms exists to up precision as needed
Conclusion
  Rough results can by used effectively

## Slide 38: Optic Box Tools Developed
Optic Box Tools
  FZP Builder
Software Packages and Tools was used for samples development
  Microsoft Visual Studio 2013 C#
  EmguCV/OpenCV – C++ computer vision library (bitmap data management part)
  FFTWSharp/FFTW – C++ Discrete Fast Fourier Transform implementation

## Slide 39: FZP Builder Optic Box Tools Developed

## Slide 40: Thank You
Contacts
  Dmitry Protopopov, Moscow, Russia dmitry@protopopov.ru +7 916 6969591
  Taras Kovtun, Boca Raton, FL, USA boss@rbadesign.us